## Slide 1: Unit 2: Working with Vector Data

## Slide 2: Working with Vector Data
File and data types: Shapefile, CSV, GeoPackage, SpatiaLite, PostGIS, MSSQL, Oracle, DB2, WMS, XYZ Tiles, WFS, ArcGIS Mapserver, GeoNode
Loading Data: Add tool, QGIS Browser, reordering layers
Layer Properties: Symbology (Single Symbol, Categorized Symbol), Label
Adding AutoCAD, MicroStation Files
Working with Layer Attribute: view/ sort attribute, select feature by expressions, add/ remove fields, calculate field
Export layer, convert geometry type

## Slide 3: GIS Data model
GIS Data model: Vector vs Raster
Characteristic | Vector | Raster
Data structure | Point, line (connected points) and polygon (closed line) Represents POI, Street, administrative border,… | AKA grid data (a regular grid of cell/ pixel)  represents continuous surfaces (digital photograph, satellite image, elevation surface,…)
Storage | Small | Large
Display and output | Map-like, smooth | Good for images, but discrete features may show “stair-step” edges Different scales between layers can be a nightmare May lose information due to generalization

## Slide 4: File and data type
Most used data format:
  Vector: Shapefile, geojson, geopackage
  Raster:
    Georeferenced: Geotiff
    Non-georeferenced: .jpg, .png,..
    GRID
  Tabular (Attributes):
    Spreadsheets: .xls, .dbf
  Combined vector/raster/tabular:
    ESRI GeoDatabase
    DBMS (PostgreSQL/PostGIS, SQLite/ SQLSpatial, MySQL, MSSQL, Oracle, DB2,…)

## Slide 5: Shapefile
Shapefile:
  A simple, nontopological format for storing the geometric location and attribute information of geographic features.
  Developed and regulated by Esri, requires at least three files to define one spatial layer.
  Only support column names <= 10 characters
  Only supports homogeneous spatial types for each layer (point/ line/ polygon)
  Only supports text fields of up to 255 characters
  File size limit at 2GB

## Slide 6: Shapefile
Shapefile:
  03 mandatory files:
    *.shp: shape (point, line or polygon)
    *.shx: shape index (search optimization)
    *.dbf: attribute (dBASE file, can open in Microsoft Access or Excel)
  Optional files:
    *.prj: coordinate and projection system information
    *.cpg: code page (should be ‘UTF-8’ for Vietnamese Unicode)
    *.xml: metadata
    *.sbn /*.sbx: spatial index that speed up loading times and optimizes spatial queries
    In QGIS: *.qpj store coordinate and projection system information for on the fly projection

## Slide 7: Shapefile
ESRI Geodatabase

## Slide 8: Shapefile
GeoPackage:
  Defined by Open Geospatial Consortium (OGC)
  Open Standard, widely used in the open source world
  A “shape file replacement” format
  Use open souce SQLite (file-base DBMS) as the storage engine
  Stores data in a single file
  Support both vector/ raster (or tiled raster) data

## Slide 9: File and data types
Other format:
  CSV (comma-separated values): Text file
  GeoJSON
  DBMS: SpatiaLite (file-based DBMS), PostGIS, MSSQL, Oracle, DB2
  Web Map Service: WMS, XYZ Tiles, WFS, ArcGIS MapServer, GeoNode

## Slide 10: File and data types
3 ways to Add data into QGIS
  Layer  Add layer
  Open Data source Manager
  Drag and drop from QGIS Browser or Window Explorer (Add to favorites for frequently used data)

## Slide 11: File and data types
Add XYZ Tile basemap
  Google Maps: https://mt1.google.com/vt/lyrs=m&x={x}&y={y}&z={z}
  HCMGIS Aerial Images: https://trueortho.hcmgis.vn/basemap/cache_lidar/{z}/{x}/{y}.jpg

## Slide 12: File and data types
Add data from Geonode:
  URL: https://opendata.hcmgis.vn

## Slide 13: Add AutoCAD file
Add AutoCAD/ MicroStation files:
  The same way with other file formats
  Export to shapefile and other formats
  Convert geometry type:
    Line <--> Polygon
    Polygon  Point (Nodes/ Centroid)
    Line  Point (Nodes/ Centroid)

## Slide 14: Working with Attribute Table
View/ sort attribute
Filter by value
Select feature by expressions
Add/ remove fields
Calculate field

## Slide 15: Some advanced Tool
Decoration
Preview Mode
Toggle Panel, Map
Show New Map View
Working with Bookmarks: Create, Show, Import, Export
Show Statistical Summary
Measure Distance
Action
Map tips
Evis Plugin
Export Map to Image, PDF

## Slide 16: Exercises
Exercises:
  Drag and drop shapefile into QGIS using Window Explorer or QGIS Browser
  Show feature count, symbology, labeling, set CRS
  Export Layer
  Add geopackage/ GeoJSON/ Geonode data, XYZ Tiles Basemap
  Calculate Field:
    Create new field for Ward Shapefile called Population, input some value
    Calculate Population Density: Population/ Area (km2)

## Slide 17: Keep Calm and enjoy Learning!
https://hcmgis.vn
HCMGIS – GIS for the City, GIS for the Community